;HxBg5_R1.ASM   -   HexBug Hack 5, Release 1 - 9/19/08

;	Personality 1

;Modified from:   HexBug Hack 5a - 1/2/08

;

;--------------------------------

;  Target Proccessor is 12F675 - No PORTA,C

; Only GPIO & TRISIO

;---------  -  ------------------

;

;********************************************************************

;                                                                 	*

;    Filename:	    ;HxBg5.ASM							   			*

;    Date:         1/2/08											*

;    File Version:	REV-5, REL-1									*

;    Author:	P.T.Miller											*

;    Company:	Applied Inspirations,LLC							*

;																	*

;********************************************************************

;	This S/W is for the HXB14c circuit board configuration-			*

;;;	 ,If using a PIC12F683- (2X Memory) >>>Note Differences<<< !!	;;;

;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;

;; NOTE:														;;

;;  This is just a starting place to get the Bug up & running.	;;

;;  With these code elements in place, many more interesting	;;

;;  behaviors/personalities can be created.						;;

;;  	Now, get busy, and be careful out there...				;;

;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;

;	GP0  -  Out, ALWAYS		Motor ON/OFF

;	GP1  -  In/Out: Vref, LED; Also J12- I/O Expantion

;	GP2  -  Out				Motor DIRECETION  ; Also J15- I/O Expantion

;	GP3  -  In, Always		Antena

;	GP4  -  In/Out: Activate/Read: Vref, Piezo; Also J14- I/O Expantion

;	GP5  -  Out:   Piezo; Also J13- I/O Expantion- Power extra I/O

;  Piezo- 		GP4,5

;  Motor ON-	GP0

;  Motor DIR-	GP2		'0'= Forward, '1'= Reverse Turn

;********************************************************************

;      	1) Initialize uC

;	Testing-

;	2) Loop till Antena touched (1 sec delay within loop)

;	3) Sound Piezo- Trill up / Wait 1 sec

;	4) Light LED / Wait 1 sec

;	5a) Run forward / Wait 1 sec

;	5b) Reverse turn / Wait 1 sec

;	5c) Run forward / Wait 1 sec

;	6) Test Battery voltage, and output via "DeciDig"/Piezo

;		WORKING- 12/27/07

;	----- Now add 'Functions' -----

;	7a) Atenae touch direction change

;	7b) 10 bumps, sounds 'complaint', restart prog.

;		WORKING- 12/28/07

;	Update Sound routines- 12/29/07, 1/1/08

;	LED 'Eye' working (Sub: PhotoStat) 1/1/08

;	'Radomize' collison sound 1/2/08

;	8) 'Dance' pattern

;		WORKING- 1/2/08

;

;**********************************************************************

;

;				FLASH	SRAM	EEPROM		I/O	 10-bit-A/D(ch)	Comp	Timers 8/16-bit

;PIC12F675  	1024 	  64 	  128 		 6 		4 			  1 	    2/1

;PIC12F683  	2048 	 128 	  256 		 6 		4 			  1 	    2/1

;

;

;**********************************************************************

TITLE "PIC12F675_HexBugHack_5"

list      p=12f675           ;  define processor

#include <p12F675.inc>       ; processor specific variable definitions

errorlevel  -302             ; suppress message 302 from list file

;	__CONFIG   _CP_OFF & _CPD_OFF & _BODEN_OFF & _MCLRE_OFF & _WDT_OFF & _PWRTE_ON & _INTRC_OSC_NOCLKOUT

__CONFIG   _CP_OFF & _CPD_OFF & _BODEN_OFF & _MCLRE_OFF & _WDT_ON & _PWRTE_ON & _INTRC_OSC_NOCLKOUT

; '__CONFIG' directive lables are located in the respective .inc file.

;**********************************

;Storage/Working Registers, in sequence:

;[From 20h to 5Fh - 64 bytes]

CBLOCK H'20'

;Interupt-

Wtmp		;'W' Temp. Storage

STATtmp		;'STATUS' Temp. Storage

;Used by Delay functions-

DLY_CNT	; low 8 bits of DeLaY CouNTer

MID_CNT	; mid 8 bits of DeLaY CouNTer

LNG_CNT	; mid 8 bits of DeLaY CouNTer

XLNG_CNT	; high 8 bits of counter for 'X'tra LoNG CouNTs

;Local temporary values-

TEMP   		;Temp High - USE ONLY WITHIN IMMIDIATE ROUTINE

TEMPL  		;Temp Low - USE ONLY WITHIN IMMIDIATE ROUTINE

;Used by Sound generating functions-

TONE		;Count for Tone

TONEDUR		;Count for Duration of Tone

SWPDUR		;Count for Duration of Sweep

TonCnt		;Tone Counter

DurCnt		;Duration Counter

SwpCnt		;Sweep Counter

TONE8		;Cont of tone cycles for musical notes

TrlRpt		;Trill Repeat Counter

TrlSwp		;Trill Sweep

WavCnt		;Wave Count

PTRNCT		;Pattern Count within table

;Misc-

Ac100s

Ac10s

OutByt		;byte to output as sound

SnoozCnt		;Snooze Cycles Counter

TrisTmp		;Temp storage of TRISIO

BmpCnt		;Count number of 'Bumps'

ClrCnt		;Count Clear (No Bump) loops

RndCnt		;Random Count

StatFlgs			;Status Flags - Bit-0

; Bit-1

; Bit-4

;

ENDC

;**********************************

;Constants:

; ANSEL bit: AN0,1,2,3 on RA0,1,2,4 / AN4,5,6,7 on RC0,1,2,3   1=Analog, 0=Digital

ANLSET			EQU		b'00000111'	;Set RC<2:0> as inputs and set RC<5:3> as outputs

ANLIN			EQU		b'00001100'	;Set RA<3:2> as inputs,and set RA<5:4,1:0> as outputs

CMPSET			EQU		b'00000111' ;Comp.OFF Setup- See Section 6.0

SWITCH			EQU		b'00001000'	;Momentary Pushbutton Switch

C			Equ		0		; Carry bit of STATUS

Carry		Equ		0		; Carry bit of STATUS

;		(((((((((((((((((((((( \ / ))))))))))))))))))))))))

;	((((((((((((((((((((((((((( V )))))))))))))))))))))))))))))

;((((((((((((((((((((( <<<<<<< (*) >>>>>>> ))))))))))))))))))))))))

;* * * * * * * *  Implementation Specific Data Values  * * * * * * * * * *

SleepCnts	EQU		d'10'	;Number of sleep cycles befor testing...

;		Sleep		; Total Sleep time cycle 4.6 sec

;		Sleep		; Total Sleep time cycle 6.9 sec

;		Sleep		; Total Sleep time cycle 9.2 sec

;		Sleep		; Total Sleep time cycle 11.5 sec

;		Sleep		; Total Sleep time cycle 13.8 sec

; 130 * 13.8 sec = 1794 sec = 29.9 min

BattLow		EQU		d'135'	;Battery voltage at knee point- 2.27-2.37v

;((((((((((((((((((((( <<<<<<< (*) >>>>>>> ))))))))))))))))))))))))

;	((((((((((((((((((((((((((( ^ )))))))))))))))))))))))))))))

;		(((((((((((((((((((((( / \ ))))))))))))))))))))))))

;    ************************************************************

;  ****************************************************************

;**********	  				CODE:						*************

;  ****************************************************************

;    ************************************************************

;**********************************************************************

ORG     0x000             ; processor reset vector

GOTO    MAIN              ; go to beginning of program

;- - - - - - - - - - - - - -

ORG     0x004             ; interrupt vector location

MOVWF   Wtmp            ; save off current W register contents

MOVF	STATUS,w          ; move status register into W register

MOVWF	STATtmp       ; save off contents of STATUS register

;/

; ISR code can go here or be located as a call subroutine elsewhere

;\

MOVF    STATtmp,w     ; retrieve copy of STATUS register

MOVWF	STATUS            ; restore pre-isr STATUS register contents

SWAPF   Wtmp,f

SWAPF   Wtmp,w          ; restore pre-isr W register contents

RETFIE                    ; return from interrupt

;------------------------------------------------------------------------------

ORG     0x010             ; interrupt vector location

;--------------------------------------

MAIN:	;These first 4 instructions are not required if the internal oscillator

; is not used, but we'll use them for future compatability-

CALL    0x3FF             ; retrieve factory calibration value

BSF     STATUS,RP0        ; set file register to BANK 1   <<--+--###

MOVWF   OSCCAL            ; update register with factory cal value

;

MOVLW	b'10001111'		; Disable Pullups; Enable PreScaler for WDT Clk, & Set to 1:128

MOVWF	OPTION_REG			;

CLRF 	ANSEL 			; Analog function turned OFF

CLRF	IOC				;Disable interupt-on-change

CLRF 	VRCON 			; Voltage Ref section turned OFF- reduce power consumption

CLRF 	INTCON			; Turn OFF Interups

;( TRISIO was set to all Inputs by RESET )

BCF     STATUS,RP0      			; Back to BANK 0   <<--+--###

CLRF 	ADCON0 			; A/D turned OFF -

;Note: The ANSEL (9Fh) and CMCON (19h)registers must be initialized to configure an

;analog channel as a digital input. Pins configured as analog inputs will read æ0Æ Digtal.

MOVLW   b'00000111'     ; Turn Comparitor OFF, Lowest Power consumption.

MOVWF   CMCON           ;  by setting CMCON<0:3>

CLRF	GPIO

TstLp1:

;**********************************************************************

;**   Delay use of MCLR, ICSPDAT, & ICSPCLK ports so Vpp can turn on

;**   programing mode before ports get re-configured and can not reprogram

;**   without being erased (5v seems to be needed for erasure)

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;**

;**********************************************************************

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVLW	b'11001000'		;Init. I/O- Motor, LED/Vref PWR, Piezo

MOVWF	TRISIO           ; Set Port A I/O:  1= Input, 0= Output

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

;  ********************************

;******  uC Setup Completed  ********

;  ********************************

BSF		GPIO,1		;LED On

MOVLW	d'2'		;Wait .1 sec

CALL	DLY_L		;@ 2.5mS per count = 5ms

BCF		GPIO,1		;LED Off

BTFSC	GPIO,3		;Loop until Antena is touched..

GOTO	TstLp1

;------------------------------------------------------------

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

;=== SOUNDS Test  =====================================

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

CALL	Trllup		;Up-Sweep Trill

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

GOTO	IOtst		;Now test I/O...

;;-------------------------------------------------------------------

;=============================================================================

;				OR... Test All SOUNDS and FUNCTIONS-

;=============================================================================

;;-------------------------------------------------------------------

CALL	Chips1

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;;-------------------------------------------------------------------

CALL	Grwl

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;;-------------------------------------------------------------------

CALL	OhUh1	;"OK?"

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;;-------------------------------------------------------------------

CALL	OhOhOh

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;;-------------------------------------------------------------------

CALL	Chips2

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;;-------------------------------------------------------------------

CALL	UhOh1

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;;-------------------------------------------------------------------

CALL	Trlldwn		;Down-Sweep Trill

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;;-------------------------------------------------------------------

CALL	Trlla

CALL	Chips1

CALL	Trlla

CALL	Trllb

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;-------------------------------------------------------------------

CALL	Trllup		;Down-Sweep Trill

CALL	Trlldwn		;Down-Sweep Trill

CALL	Trllb

;-------------------------------------------------------------------

IOtst:

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVLW	b'11001000'		; Define I/O

MOVWF	TRISIO           ; Set Port A I/O:  1= Input, 0= Output

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

;-- Test GPIO-1, Test LED  (Pin 6)

BSF		GPIO,1

MOVLW	d'5'		;Wait .5 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,1		;LED Off

;-- Test GPIO-0, Motor ON, FWD	 (Pin 7)

;Fwrd: - Rvrs:

;		BSF		GPIO,2		;Direction

;		BSF		GPIO,0		;Motor ON

CALL	Fwrd

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,0		;Motor OFF

MOVLW	d'20'

CALL	DLY_L		;@ 2.5mS per count = 50ms

;NOTE: Always turn motor OFF BEFORE CHANGING DIRECTION to prevent 'shoot-thru'

;-- Test GPIO-2, Direction-REV  (Pin 5)

;		BCF		GPIO,2

;		BSF		GPIO,0		;Motor ON

CALL	Rvrs

MOVLW	d'15'		;Wait 1.5 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,0		;Motor OFF

MOVLW	d'20'

CALL	DLY_L		;@ 2.5mS per count = 50ms

;-- Test GPIO-2, Direction-FWD  (Pin 5)

;		BSF		GPIO,2		;Direction

;		BSF		GPIO,0		;Motor ON

CALL	Fwrd

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;-Turn Motor OFF-

BCF		GPIO,0		;Motor Off

MOVLW	d'5'		;Wait 1/2 sec

CALL	DLY_X		;100ms/Cycle

;;---------------------------------------------------------------------

;PhotLvl:

;;Read Phot Voltage level-

;		CLRWDT

;;Uses Right-Justified, Low Byte is in BANK-1

;		CALL	PhotoStat	;Returns with light level in 'W'

;		MOVWF	OutByt		;Save for converstion...

;;Convert value passed in OutByt to 3 Decimal Digits:

;		CALL	DeciDig		;Output value a 'Beeps'

;

;		MOVLW	d'10'		;Wait 1 sec

;		CALL	DLY_X		;100ms/Cycle

;

;			CALL	Tone2

;			CALL	Tone3

;		MOVLW	d'10'		;Wait 1 sec

;		CALL	DLY_X		;100ms/Cycle

;;-------------------------------------------------------------------

;=============================================================================

;=============================================================================

;;-------------------------------------------------------------------

BattLvl:

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVLW	b'11001000'		; Define I/O

MOVWF	TRISIO           ; Set Port A I/O:  1= Input, 0= Output

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

;Read Battery Voltage level-

CLRWDT

CLRF	ADRESH

CALL	BattStat

MOVF	ADRESH,W	;Get voltage level

;		MOVLW	d'237'		; FOR TESTING--

;		MOVLW	d'23'		; FOR TESTING--

MOVWF	OutByt		;Save for converstion...

;Convert value passed in OutByt to 3 Decimal Digits:

CALL	DeciDig		;Output value as 'Beeps'

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

CALL	Tone3

CALL	Tone2

;			CALL	BEEP

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

;--------------  Wait for antenna touch to go into full opperation   -------------

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

OprLP:

MOVLW	d'10'		;Wait 1 sec

CALL	DLY_X		;100ms/Cycle

BSF		GPIO,1		;LED On

MOVLW	d'2'		;Wait .1 sec

CALL	DLY_L		;@ 2.5mS per count = 5ms

BCF		GPIO,1		;LED Off

BTFSC	GPIO,3		;Loop until Antena is touched..

GOTO	OprLP

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

;---------------------------------------------------------------------

RUNN:

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVLW	b'11001000'		;Init. I/O- Motor, LED/Vref PWR, Piezo

MOVWF	TRISIO           ; Set Port A I/O:  1= Input, 0= Output

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

CALL	Trllup		;Up-Sweep Trill

;---------------------------------------------------------------------

;Init. 'Bump' & 'Clear' Counters-

MOVLW	.10			;Obstical Bumps till re-start-

MOVWF	BmpCnt

CLRF	ClrCnt		;Clear the 'No Bumps' Count

FwrdLp:

;--------------------------------------------------------------------------

;;;;;  ADD BATT TEST -----------

;--------------------------------------------------------------------------

INCF	ClrCnt,F

;-- GPIO-0, Motor ON, FWD	 (Pin 7)

CALL	Fwrd			;MOTOR ON FORWARD <<--=========<<<

;--------------------------------------------------------------------------

;For Testing- Remove to consrve Power -

BSF		GPIO,1		;LED On

MOVLW	d'2'

CALL	DLY_L		;@ 2.5mS per count = 5ms

BCF		GPIO,1		;LED Off

MOVLW	d'100'

CALL	DLY_L		;@ 2.5mS per count = .25 sec

;--------------------------------------------------------------------------

;If ClrCnt = 120, (30sec) Celebrate-

MOVLW	.120		;Set 'W' to actuate count

XORWF	ClrCnt,W

BTFSC	STATUS,Z	; skip next if not ZERO...

GOTO	Celbrt

;-------------------------<<<<<<<<<<<<<<<<<<<<<----------------------------

BTFSC	GPIO,3		;Loop until Antena is touched..

GOTO	FwrdLp		;NO BUMP- FORWARD LOOP...

;.............

BCF		GPIO,0		;Motor OFF

MOVLW	d'1'		;Wait .1 sec

CALL	DLY_X		;100ms/Cycle

;==================================SSSSSSSSSSSSSSSSSSSSSSSSSSSS============

CALL	BmpSnd		;Semi-Random selection of bump sound

DECF	BmpCnt,F	;Dec Bump Count-

CLRF	ClrCnt		;Clear the 'No Bumps' Count (start over)

;Reverse turn 90 Deg.-

;---------------------------

;;on 9th bump, throw tantrum-

;		MOVLW	.9		;Set 'W' to actuate count

;		XORWF	BmpCnt,W

;		BTFSC	STATUS,Z	; skip next if not ZERO...

;			GOTO	TanTrm

;---------------------------

;On 10th bump, throw tantrum-

MOVF	BmpCnt,W

ANDWF	BmpCnt,W	;Set Z

BTFSC	STATUS,Z	; skip next if not ZERO...

GOTO	TanTrm

;---------------------------

CALL	Rvrs

MOVLW	d'15'		;Wait 1.5 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,0		;Motor OFF

MOVLW	d'20'

CALL	DLY_L		;@ 2.5mS per count = 50ms

GOTO	FwrdLp

;================================================================

TanTrm:

CALL	Grwl

BCF		GPIO,0		;Motor OFF

MOVLW	d'2'		;Wait .2sec

CALL	DLY_X		;100ms/Cycle

CALL	Grwl

;............

CALL	Rvrs

MOVLW	d'3'		;Wait .3 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,0		;Motor OFF

CALL	Chips2

CALL	Fwrd

MOVLW	d'3'		;Wait .3 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,0		;Motor OFF

CALL	Rvrs

MOVLW	d'4'		;Wait .4 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,0		;Motor OFF

CALL	Chips2

CALL	Fwrd

MOVLW	d'5'		;Wait .5 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,0		;Motor OFF

;............

CALL	Grwl

CALL	Rvrs

MOVLW	d'3'		;Wait .3 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,0		;Motor OFF

CALL	Chips2

CALL	Fwrd

MOVLW	d'3'		;Wait .3 sec

CALL	DLY_X		;100ms/Cycle

;............

CALL	Rvrs

MOVLW	d'3'		;Wait .3 sec

CALL	DLY_X		;100ms/Cycle

BCF		GPIO,0		;Motor OFF

CALL	Trlldwn

MOVLW	d'200'		;Wait 20 sec

CALL	DLY_X		;100ms/Cycle

GOTO	RUNN		;Start New

;================================================================

;30 sec no bumps-

Celbrt:

BCF		GPIO,0		;Motor OFF

MOVLW	d'2'		;Wait .2sec

CALL	DLY_X		;100ms/Cycle

CALL	OhUh1	;"OK?"

MOVLW	d'10'		;Wait 1sec

CALL	DLY_X		;100ms/Cycle

;=====================================================

;======     Turn in reverse while 'singing'     ======

;==== (Create more interseting SONG & DANCE here) ====

CALL	Rvrs

CALL	Trllup		;Up-Sweep Trill

MOVLW	d'4'		;Wait .4 sec

CALL	DLY_X		;100ms/Cycle

CALL	Trlldwn

MOVLW	d'4'		;Wait .4 sec

CALL	DLY_X		;100ms/Cycle

CALL	Trlla

CALL	Trllb

CALL	Trlla

CALL	Trllup		;Up-Sweep Trill

MOVLW	d'4'		;Wait .4 sec

CALL	DLY_X		;100ms/Cycle

CALL	Trlldwn

MOVLW	d'4'		;Wait .4 sec

CALL	DLY_X		;100ms/Cycle

;======                                         ======

;=====================================================

BCF		GPIO,0		;Motor OFF

MOVLW	d'100'		;Wait 10sec

CALL	DLY_X		;100ms/Cycle

CALL	Trlla

CALL	Chips1

CALL	Trlla

CALL	Trllb

;=====   Now, Do it all over again   =====

GOTO	RUNN		;Start New

;* * * * * * * * * * * * * * * * * * * * * * * * *

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

;  Use this code block to setup 'Sleep' mode, very low power-

;====================================================================

;=======SSSSSSSSSSSSSSSSSSS  sleep  SSSSSSSSSSSSSSSSSSSSSSSSS========

SleepLoop:

; Save power during SLEEP:

MOVLW	SleepCnts	;Set number of SLEEP Cycles

MOVWF	SnoozCnt

CALL	PwrDwn	;Lowet power condition, modifies port config. to All Inputs-

SnoozLoop:

Sleep		;SLEEP clears WDT, full 2.3 sec WDT cycle begins.

;Check Switch after each SLEEP to reduce responce time...

BTFSS	GPIO,3			; test SWITCH input (Skip if set(High), Button Not Pressed)

GOTO	WAKE			; Button pushed Exit Sleep Cycles...

DECFSZ	SnoozCnt,F		;Dec Snooze counter, Skip GOTO if tim to wake

GOTO	SnoozLoop

; Total Sleep time cycle: 130 * 13.8 sec = 1794 sec = 29.9 min

;		CLRF	ANSEL		;Turned OFF Analog functions <<< DONE IN PwrDwn

;	CALL	Note_A0		;<<< FOR TESTING - Beep at wake-up

; -  -  -  -  -  -  -  -

WAKE:

;-------------------------------------------

; Test Mom.Sw for activity-

; PortA, Bit-3 is Mom.SW , Normaly tied HIGH. Activation pulls it to GND

; PwrDwn has already put GPIO in the input state.

ChkSW:

BTFSC	GPIO,3		; test SWITCH input (Skip if clear(Low), Bit LOW, Button Pressed)

GOTO	TempSkp		; Button not pushed...

;XXXXXXXXXXXXXXXXX   INPUT  BUTTON  PRESSED  XXXXXXXXXXXXXXXXXXXXXXX

; No Debouncing of the input switch is needed; once dedected that it's been pressed,

; the TREE call will delay longer than the bounce time.

TempSkp:

NOP

;Additional Code Here..........

;------------------------------------------------

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

;=======================================================================================

;====================================================================

;-------------------  Sound Effect Sub.s   -----------------------

;====================================================================

;=======================================================================================

;Bump Sound- Semi Random selection of sound. Depends upon ClrCnt & BmpCnt-

; Routine jumps to sound effect, and returns from there...

BmpSnd:

MOVLW	.8			;No complaints on 1st 3 bumps-

SUBWF	BmpCnt,W	;BmpCnt-7=>W, C,Z

BTFSC	STATUS,C	; skip next if Borrow (carry=0) occured...

RETURN				;If it's the 1st 3 bumps, no sound

;.............................

MOVF	BmpCnt,W

ADDWF	ClrCnt,W

MOVWF	RndCnt		;Store selection

MOVLW	b'00001111'

ANDWF	RndCnt,F	;Limit count to 0-15

;........................

SelctSnd:

DECFSZ	RndCnt,F

GOTO	$+2		;Skip Next

;Jump is inside a CALL, the routine jumped to will provide the return.

GOTO	UhOh1		;1

DECFSZ	RndCnt,F

GOTO	$+2

;		GOTO	Trllup		;2

GOTO	Grwl		;2

DECFSZ	RndCnt,F

GOTO	$+2

GOTO	Trlldwn		;3

DECFSZ	RndCnt,F

GOTO	$+2

GOTO	Chips1		;4

DECFSZ	RndCnt,F

GOTO	$+2

GOTO	Grwl		;5

DECFSZ	RndCnt,F

GOTO	$+2

GOTO	OhOhOh		;6

DECFSZ	RndCnt,F

GOTO	$+2

GOTO	OhUh1		;7

DECFSZ	RndCnt,F

GOTO	$+2

RETURN				;8 - No Sound

DECFSZ	RndCnt,F

GOTO	$+2

GOTO	Trlla		;9

DECFSZ	RndCnt,F

GOTO	SelctSnd	;If no match, loop around again

GOTO	Trllb

;=======================================================================================

;-------------------------------------------------------------------

;-------------------------------------------------------------------

; Growl-

Grwl:

CALL	Grrr

MOVLW	d'7'		;Wait xms

CALL	DLY_L		;2.5ms/Cycle

CALL	Grrr

MOVLW	d'7'		;Wait xms

CALL	DLY_L		;2.5ms/Cycle

CALL	Grrr

RETURN				;Done

;-------------------------------------------------------------------

Grrr:

MOVLW	.60			;number of waves

MOVWF	WavCnt

MOVLW	.65			;number of 1/2 waves

MOVWF	TONEDUR		;WavCnt

GrrWv:

MOVF	TONEDUR,W		;WavCnt

MOVWF	TonCnt		;WavCnt

;........................

BSF		STATUS,RP0		;Switch to BANK 1   <<--+--###

BCF		TRISIO,4           ; Set Port A I/O:  1= Input, 0= Output

BCF		TRISIO,5           ; Set Port A I/O:  1= Input, 0= Output

BCF		STATUS,RP0		; Switch Back to BANK 0   <<--+--###

;Set complementary Piezo output bits

BSF		GPIO, 4

BCF		GPIO, 5

;----------------------------------------

Grr_LP:

;Create Pulse-

MOVLW	b'00110000'	;								(1)

XORWF	GPIO,F		;Flip port bits to sound Piezo	(1)

;----------------------------------------

MOVLW	.11		;1st Peak Res.of Kobitone Piezo	(1)

;*		MOVLW	.17		;2nd Peak Res.of Kobitone Piezo	(1)

MOVWF   DLY_CNT ; Store loop cnt	(1)

GR1_LP:														;2+(11*7)= 79

;*GR1_LP:														;2+(17*7)= 121

NOP					;						(1)

NOP					;						(1)

NOP					;						(1)

CLRWDT					;Clear WDT			(1)

DECFSZ  DLY_CNT,F       ; 					(1/2)

GOTO    GR1_LP     	; 7uS/loop		    (2)

;----------------------------------------

DECFSZ  TonCnt,F			; 				(1/2)		79+3+5=87

;*		DECFSZ  TonCnt,F			; 				(1/2)		121+3+5=129

GOTO    Grr_LP		;			    (2)

;Space between pulses-

MOVLW	d'6'		;Wait 80us

CALL	DLY_S		;10us/Cycle

;		INCF	TONEDUR,F	;Increase the tone duration

DECF	TONEDUR,F	;Reduce the tone duration

DECFSZ  WavCnt,F

GOTO    GrrWv

;Relax Piezo-

BCF		GPIO, 4

BCF		GPIO, 5

RETURN				;Done

;-------------------------------------------------------------------

;-------------------------------------------------------------------

UhOh1:

MOVLW	.120

MOVWF	TONE			;Set TONE count

;		MOVLW	.25

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

MOVLW	.20

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepU

MOVLW	d'1'		;Wait .1 sec

CALL	DLY_X		;100ms/Cycle

MOVLW	.180

MOVWF	TONE			;Set TONE start count

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

MOVLW	.24

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepD

;Hold end of sweep note-

MOVLW	.50

MOVWF	TONEDUR			;Set TONE Duration

MOVF	TonCnt,W		;Get Tone count at end of sweep into 'W' to pass to Sub

CALL	MkTone

RETURN

;-------------------------------------------------------------------

;-------------------------------------------------------------------

OhOhOh:

;		MOVLW	.180

MOVLW	.80

MOVWF	TONE			;Set TONE start count

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

MOVLW	.34

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepD

;Hold end of sweep note-

MOVLW	.180

MOVWF	TONEDUR			;Set TONE Duration

MOVF	TonCnt,W		;Get Tone count at end of sweep into 'W' to pass to Sub

CALL	MkTone

MOVLW	d'1'		;Wait .1 sec

CALL	DLY_X		;100ms/Cycle

;++++++++++++++++++

;		MOVLW	.140

MOVLW	.100

MOVWF	TONE			;Set TONE start count

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

;		MOVLW	.24

MOVLW	.30

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepD

;Hold end of sweep note-

MOVLW	.120

MOVWF	TONEDUR			;Set TONE Duration

MOVF	TonCnt,W		;Get Tone count at end of sweep into 'W' to pass to Sub

CALL	MkTone

MOVLW	d'1'		;Wait .1 sec

CALL	DLY_X		;100ms/Cycle

;++++++++++++++++++

MOVLW	.200

MOVWF	TONE			;Set TONE start count

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

;		MOVLW	.24

MOVLW	.30

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepD

;Hold end of sweep note-

MOVLW	.80

MOVWF	TONEDUR			;Set TONE Duration

MOVF	TonCnt,W		;Get Tone count at end of sweep into 'W' to pass to Sub

CALL	MkTone

RETURN

;-------------------------------------------------------------------

;-------------------------------------------------------------------

;Sound like "OK?"

OhUh1:

MOVLW	.180

MOVWF	TONE			;Set TONE start count

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

MOVLW	.24

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepD

MOVLW	d'1'		;Wait .1 sec

CALL	DLY_X		;100ms/Cycle

;		MOVLW	.120

MOVLW	.100

MOVWF	TONE			;Set TONE count

MOVLW	.25

;		MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

MOVLW	.20

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepU

;Hold end of sweep note-

MOVLW	.80

MOVWF	TONEDUR			;Set TONE Duration

MOVF	TonCnt,W		;Get Tone count at end of sweep into 'W' to pass to Sub

CALL	MkTone

RETURN

;-------------------------------------------------------------------

;-------------------------------------------------------------------

Trlla:

MOVLW	.8

MOVWF	TrlRpt		;ToneRepeat count

Trll:

MOVLW	.50

MOVWF	TONE			;Set TONE start count

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

MOVLW	.20

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepU

MOVLW	d'20'		;Wait 50ms

;		CALL	DLY_L		;2.5ms/Cycle

DECFSZ	TrlRpt,F

GOTO	Trll

MOVLW	.8

MOVWF	TrlRpt		;ToneRepeat count

Trll2:

MOVLW	.70

MOVWF	TONE			;Set TONE start count

MOVLW	.12

MOVWF	TONEDUR			;Set TONE Duration

;(Use same Sweep Duration)

CALL	SweepU

MOVLW	d'20'		;Wait 50ms

;		CALL	DLY_L		;2.5ms/Cycle

DECFSZ	TrlRpt,F

GOTO	Trll2

RETURN

;--------------------------------------------------------------------------------

;--------------------------------------------------------------------------------

Trllb:

MOVLW	.8

MOVWF	TrlRpt		;ToneRepeat count

Trll3:

MOVLW	.50

MOVWF	TONE			;Set TONE start count

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

CALL	SweepD

MOVLW	d'20'		;Wait 50ms

;		CALL	DLY_L		;2.5ms/Cycle

DECFSZ	TrlRpt,F

GOTO	Trll3

MOVLW	.11

MOVWF	TrlRpt		;ToneRepeat count

Trll4:

MOVLW	.70

MOVWF	TONE			;Set TONE start count

MOVLW	.12

MOVWF	TONEDUR			;Set TONE Duration

CALL	SweepD

MOVLW	d'20'		;Wait 50ms

;		CALL	DLY_L		;2.5ms/Cycle

DECFSZ	TrlRpt,F

GOTO	Trll4

RETURN

;--------------------------------------------------------------------------------

;--------------------------------------------------------------------------------

;Sweep trill Up-

Trllup:

MOVLW	.30

MOVWF	TrlSwp		;Trill Repeat count for sweep

MOVLW	.30

MOVWF	TONE			;Set TONE start count

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

MOVLW	.15

MOVWF	SWPDUR			;Set Duration of sweep

Trll6:

MOVLW	.2

MOVWF	TrlRpt		;ToneRepeat count

Trll5:

CALL	SweepD

CLRWDT

;		MOVLW	d'20'		;Wait 50ms

;		CALL	DLY_L		;2.5ms/Cycle

DECFSZ	TrlRpt,F

GOTO	Trll5

;...................

DECF	TONE,F

DECFSZ	TrlSwp,F

GOTO	Trll6

RETURN

;--------------------------------------------------------------------------------

;--------------------------------------------------------------------------------

;Sweep trill Down-

Trlldwn:

MOVLW	.30

MOVWF	TrlSwp		;Trill Repeat count for sweep

MOVLW	.10

MOVWF	TONE			;Set TONE start count

MOVLW	.12

MOVWF	TONEDUR			;Set TONE Duration

Trll8:

MOVLW	.2

MOVWF	TrlRpt		;ToneRepeat count

Trll7:

CALL	SweepD

CLRWDT

;		MOVLW	d'20'		;Wait 50ms

;		CALL	DLY_L		;2.5ms/Cycle

DECFSZ	TrlRpt,F

GOTO	Trll7

;...................

;		INCF	TONE,F

;		INCF	TONE,F

INCF	TONE,F

INCF	TONE,F

DECFSZ	TrlSwp,F

GOTO	Trll8

RETURN

;--------------------------------------------------------------------------------

;--------------------------------------------------------------------------------

Chips1:

MOVLW	.20

MOVWF	TrlRpt		;ToneRepeat count

Chp2LP:

MOVLW	.25

MOVWF	TONE			;Set TONE start count

MOVLW	.15

MOVWF	TONEDUR			;Set TONE Duration

MOVLW	.10

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepU

MOVLW	d'10'		;Wait 25ms

CALL	DLY_L		;2.5ms/Cycle

DECFSZ	TrlRpt,F

GOTO	Chp2LP

RETURN

;--------------------------------------------------------------------------------

;--------------------------------------------------------------------------------

Chips2:

MOVLW	.7

MOVWF	TrlRpt		;ToneRepeat count

Chp1LP:

MOVLW	.50

MOVWF	TONE			;Set TONE start count

MOVLW	.55

MOVWF	TONEDUR			;Set TONE Duration

MOVLW	.5

MOVWF	SWPDUR			;Set Sweep Duration

CALL	SweepU

MOVLW	d'100'		;Wait 25ms

CALL	DLY_L		;2.5ms/Cycle

DECFSZ	TrlRpt,F

GOTO	Chp1LP

RETURN

;--------------------------------------------------------------------------------

;--------------------------------------------------------------------------------

;	--- SWEEPS ---

;Tone/TonDur: 50/25- Drip sound, 30/25- Higher Drip

;If tone value is to short, tone 'Wraps-around'

;--------------------------------------------------------------------

;Sweep-Up  Enter with TONE, TONEDUR, & SWPDUR set.

;These values will NOT be CHANGED, but used to set:

;	DLY_CNT, TonCnt, DurCnt, & SwpCnt

SweepU:

; Init. I/O -

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVF	TRISIO,W           ; Save I/O state-

MOVWF	TrisTmp

BCF		TRISIO,4         ; Set Port A I/O for Output on 4,5

BCF		TRISIO,5         ; Set Port A I/O for Output on 4,5

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

BSF		GPIO, 4		;Set complementary Piezo output bits

BCF		GPIO, 5

;------------------------------------

MOVF	TONE,W

MOVWF	TonCnt

MOVF	TONEDUR,W

MOVWF	DurCnt

SwpLP2:

;				MOVLW	d'8'		;									1

MOVF	SWPDUR,W	;Get # of cycles of tone

MOVWF	SwpCnt		;Init Tone Cycles					1

;------------------------------------

SwpLP:

MOVF	TonCnt,W			;Get Value for Tone Delay:			1

MOVWF   DLY_CNT 		; Store loop cnt passed in 'W'		1

;------------------------------------

SWP_LP:

DECFSZ    DLY_CNT,F		; Dec TONE count & Skp if Zero		1 (2)

GOTO    SWP_LP         ; Not zero, so loop				2  V

MOVLW	b'00110000'     ;     								1

XORWF	GPIO,F			;Flip port bits to sound Piezo		1

;------------------------------------

DECFSZ	SwpCnt,F			;Dec Cycle Counter & Skip if Z	1   ((2))Exit

GOTO	SwpLP			;								2

;------------------------------------

DECF	TonCnt,F		;Increase Pitch

DECFSZ	DurCnt,F			;Dec DurCnt & Skip if Zero		1 (2)

GOTO	SwpLP2			;								2  V

;------------------------------------

;Relax Piezo-

BCF		GPIO, 4

BCF		GPIO, 5

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVF	TrisTmp,W       ;Get I/O state-

MOVWF	TRISIO			;& restore it...

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

Return

;--------------------------------------------------------------------

;--------------------------------------------------------------------

;Sweep-Down  Enter with TONE, TONEDUR, & SWPDUR set.

;These values will NOT be CHANGED, but used to set:

;	DLY_CNT, TonCnt, DurCnt, & SwpCnt

SweepD:

; Init. I/O -

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVF	TRISIO,W           ; Save I/O state-

MOVWF	TrisTmp

BCF		TRISIO,4         ; Set Port A I/O for Output on 4,5

BCF		TRISIO,5         ; Set Port A I/O for Output on 4,5

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

BSF		GPIO, 4		;Set complementary Piezo output bits

BCF		GPIO, 5

;------------------------------------

MOVF	TONE,W

MOVWF	TonCnt

MOVF	TONEDUR,W

MOVWF	DurCnt

SwpDLP2:

;				MOVLW	d'8'		;									1

MOVF	SWPDUR,W	;Get # of cycles of tone

MOVWF	SwpCnt		;Init Tone Cycles					1

;------------------------------------

SwpDLP:

MOVF	TonCnt,W			;Get Value for Tone Delay:			1

MOVWF   DLY_CNT 		; Store loop cnt passed in 'W'		1

;------------------------------------

SWPD_LP:

DECFSZ    DLY_CNT,F		; Dec TONE count & Skp if Zero		1 (2)

GOTO    SWPD_LP         ; Not zero, so loop				2  V

MOVLW	b'00110000'     ;     								1

XORWF	GPIO,F			;Flip port bits to sound Piezo		1

;------------------------------------

DECFSZ	SwpCnt,F			;Dec Cycle Counter & Skip if Z	1   ((2))Exit

GOTO	SwpDLP			;								2

;------------------------------------

INCF	TonCnt,F		;Decrease Pitch

DECFSZ	DurCnt,F			;Dec DurCnt & Skip if Zero		1 (2)

GOTO	SwpDLP2			;								2  V

;------------------------------------

;Relax Piezo-

BCF		GPIO, 4

BCF		GPIO, 5

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVF	TrisTmp,W       ;Get I/O state-

MOVWF	TRISIO			;& restore it...

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

;---------------

Return

;--------------------------------------------------

;--------------------------------------------------

;256 Cycles at Freq. set duration passed in 'W'.

; Base for all tones. BEEP turns ON needed I/O, Then turns it OFF when done.

BEEP:

MOVWF	TONE			;Save TONE passed in W

; Enter HERE if TONE is set elsewhere....

BEEPTN:		;(Call here if tone is deifined externaly)

MOVLW	d'180'

MOVWF	TEMPL			;Set Length of Beep

; Enter HERE if TONE & TEMPL are set elsewhere....

BEEPTLN:	;(Call here if tone & length of beep deifined externaly)

;	Piezo- GP4,5

;;		CLRF	GPIO

BSF		STATUS,RP0		;Switch to BANK 1   <<--+--###

;		MOVLW	b'11111010'		; Define I/O for Peizo.....

;		MOVWF	TRISIO           ; Set Port A I/O:  1= Input, 0= Output

BCF		TRISIO,4           ; Set Port A I/O:  1= Input, 0= Output

BCF		TRISIO,5           ; Set Port A I/O:  1= Input, 0= Output

BCF		STATUS,RP0		; Switch Back to BANK 0   <<--+--###

;Set complementary Piezo output bits

BSF		GPIO, 4

BCF		GPIO, 5

BEEPLP:

MOVF	TONE,W			;Get Value for Tone Delay:

CALL	DLY_S			;Delay = 10uS * 'W'

;WAS		MOVLW	b'00010001'

MOVLW	b'00110000'

XORWF	GPIO,F			;Flip port bits to sound Piezo

DECFSZ	TEMPL,F		; Check for end of min durration

GOTO	BEEPLP

Return

;--------------------------------------------------------------------

;--------------------------------------------------------------------

;******************************

Tone0:

MOVLW	d'50'

MOVWF	TONEDUR		;Save Duration passed in W

MOVLW	d'237'		;Tone - G (Fa)

GOTO	MkTone		;(sub will store TONE)

;----------------

Tone1:

MOVLW	d'101'

MOVWF	TONEDUR		;Save Duration passed in W

MOVLW	d'117'		;Tone - G (Fa)

GOTO	MkTone		;(sub will store TONE)

;----------------

Tone2:

MOVLW	d'190'		;* 8 cycles of tone = .288 sec of tone

MOVWF	TONEDUR		;Save Duration passed in W

MOVLW	d'29'		;Tone - E (Re)

GOTO	MkTone		;(sub will store TONE)

;----------------

Tone3:

MOVLW	d'226'		;* 8 cycles of tone = .288 sec of tone

MOVWF	TONEDUR		;Save Duration passed in W

MOVLW	d'24'		;Tone - G (Fa)

GOTO	MkTone		;(sub will store TONE)

;=================================================================

; Make Tone Subroutine- Recieves TONE value in 'W'

; Duration already set in TONEDUR.

; Counts out bit transitions to set duration for each note -

; Not dependent on hardware- WDT or Interups

MkTone:

CLRWDT

MOVWF	TONE			;Save TONE passed in W

; Init. I/O -

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

;		MOVLW	b'11001111'		; Define I/O

;		MOVWF	TRISIO           ; Set Port A I/O:  1= Input, 0= Output

MOVF	TRISIO,W           ; Save I/O state-

MOVWF	TrisTmp

BCF		TRISIO,4         ; Set Port A I/O for Output on 4,5

BCF		TRISIO,5         ; Set Port A I/O for Output on 4,5

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

BSF		GPIO, 4		;Set complementary Piezo output bits

BCF		GPIO, 5

MkoteLP2:

MOVLW	d'8'		;										1

MOVWF	TONE8		;Init for 8 Cycles of Tone				1

MkoteLP:

MOVF	TONE,W			;Get Value for Tone Delay:			1

MOVWF   DLY_CNT 		; Store loop cnt passed in 'W'		1

Nk_LOOP:

DECFSZ    DLY_CNT,F		; Dec TONE count & Skp if Zero		1 (2)

GOTO    Nk_LOOP         ; Not zero, so loop				2  V

MOVLW	b'00110000'     ;     								1

XORWF	GPIO,F			;Flip port bits to sound Piezo		1

DECFSZ	TONE8,F			;Dec 8 Cycle Counter & Skip if Z	1   ((2))Exit

GOTO	MkoteLP			;								2

DECFSZ	TONEDUR,F			;Dec TONDUR & Skip if Zero		1 (2)

GOTO	MkoteLP2			;								2  V

;---------------

;Relax Piezo-

BCF		GPIO, 4

BCF		GPIO, 5

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVF	TrisTmp,W       ;Get I/O state-

MOVWF	TRISIO			;& restore it...

BCF     STATUS,RP0      ; Set Bank 0   <<--+--###

;---------------

Return

;====================================================================

;=============================================================================

;----------------------  Motion Sub.s   --------------------------

;=============================================================================

;Motor ON, FWD	 (Pin 7)

Fwrd:

BCF		GPIO,0		;Assure Motor is OFF to prevent 'Shoot-Thru'

MOVLW	d'10'

CALL	DLY_L		;@ 2.5mS per count = 25ms

BSF		GPIO,2		;Set FORWARD Direction

BSF		GPIO,0		;Motor ON

RETURN

;--------------------------------------------------

;--------------------------------------------------

;Motor ON, REV	 (Pin 7)

Rvrs:

BCF		GPIO,0		;Assure Motor is OFF to prevent 'Shoot-Thru'

MOVLW	d'10'

CALL	DLY_L		;@ 2.5mS per count = 25ms

BCF		GPIO,2		;Set REVERSE Direction

BSF		GPIO,0		;Motor ON

RETURN

;--------------------------------------------------

;--------------------------------------------------

;Motor OFF, FWD	 (Pin 7)

STOP:

BSF		GPIO,2		;Set FWD Direction

BCF		GPIO,0		;Motor OFF

RETURN

;=============================================================================

;----------------------  Utillity Sub.s   --------------------------

;=============================================================================

;-------------------------------------------------------

;Get Battery status:

;	NOTE: RECALCULATE FOR 2x 1.25 volt NiMh batteries

;Set up ADC using Vcc as ref. Turn on Vref (GP0), and measure AN-1. If Vcc is 2.5VDC,

; then 1.22 Vref will read as 47.84% of the ADC. With a Max count of 1024, 490 = Vcc = 2.5vdc.

;At a min battery voltage of 2.2, the ADC would read Vref as 568.

; At Vbat of 4.9vdc, Vref would read 255.

;Since the ADC output is 10bits, and the buss is 8bits, both ADRESH, & ADRESL need

;to be read if the data is right justified.

; If it is left justified, only ADRESh needs to be read, and the value considerd to be

;divided by 4. [Note: ADRESH is accessed in Bank-0, while ADRESL is in Bank-1.]

; For the selected voltages:  2.5vdc => 122; 2.2vdc => 142;

; ADC registers for config: ADCON0, ADCON1, ANSEL

;The ANS7:ANS0 bits (ANSEL<7:0>) and the TRISIO bits control the operation of the A/D

;port pins. Set the corresponding TRISIO bits to set the pin output driver to its high

;impedance state. Likewise, set the corresponding ANS bit to disable the digital

;input buffer. [Note: Analog voltages on any pin that is defined as a digital input

; may cause the input buffer to conduct excess current.]

;[Note: The GO/DONE bit should not be set in the same instruction that turns on the A/D.]

BattStat:

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

;Set GP-1 as digital out (turn on Vref), All others a 3st via TRISIO :

;			 bit: 76543210

MOVLW	b'11111101'

MOVWF	TRISIO

;			 bit: 76543210 (Low 4 bits selcet enabled channel/s)

MOVLW   b'01011000'     ;AN3 enabled as Analog for ADC

; Set ADC Clock - Osc/16 = 4uS (1.6uS is minimum, but 4uS assures opperation at less than 3 Vdc.)

; Select/Enable Analog Channels (AN-1)

MOVWF   ANSEL

BCF     STATUS,RP0      ; Back to Bank 0   <<--+--###

;	-------------------------------------------------------

BSF		GPIO,1		;Turn on External 'Vref' to be read on AN3

;			 bit: 76543210 (bit 2,3 select channel to convert from)

MOVLW   b'00001101'

; Set: LEFT-JUSTIFIED, Vref to Vdd, Select Chanel AN-3, turn on ADC

MOVWF   ADCON0

; The minimum acquisition time is 20uS for the Sample & Hold capacitor to settle,

; Allow 150ms for things to settle:

;xxxx;TEMP <<<<<<<<<<<<<<<<<<,,

;		MOVLW	d'250'		;.625 sec

;		Call	DLY_L		;delay for 2.5mS/loop

MOVLW	d'5'		; .5 sec

Call	DLY_X		;delay for 100mS/loop

;Start ADC Conversion by turning GO/Done, bit-1 ON.

BSF		ADCON0,1

; The minimum acquisition time is 20uS for the Sample & Hold capacitor to settle,

MOVLW	d'60'

Call	DLY_L		;delay for 2.5mS x 60 = 150mS

;-------------------------------------

;Conversion takes Min. 11 x ADC Clock = 11x4uS = 44uS:

ADCDLY:

;		MOVLW	d'6'

MOVLW	d'20'	;try 200us

Call	DLY_S		;delay for 10uS x 6 = 60uS

;Check for conversion complete:

BTFSC	ADCON0,1		;Skip next if 'DONE'bit = 0 ; Conversion Complete.

GOTO	ADCDLY			;Delay again till conversion is complete, or WDT resets...

; Conversion Complete- Battery Status Value is now in 'ADRESH'; Turn off ADC.

;	-------------------------------------------------------

BCF		GPIO,1		;Turn OFF External 'Vref' to be read on AN3

;		Call	PwrDwn			;[Also turns off all analog inputs.]

Return

;=============================================================================

;=============================================================================

;-------------------------------------------------------

; (See 'BattStat' for details)

;Read LED used as solar cell, Return Vale in 'W'-

PhotoStat:

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

CLRF	ADRESL		;Clear old data

;Clear Charge on LED-

;			 bit: 76543210

MOVLW	b'11111101'

MOVWF	TRISIO

;			 bit: 76543210 (Low 4 bits selcet enabled channel/s)

MOVLW   b'01010000'     ;Disable Analog

MOVWF   ANSEL

BCF     STATUS,RP0      ; Back to Bank 0   <<--+--###

BCF		GPIO,1		;Pull LED LOW

MOVLW	d'60'

Call	DLY_L		;delay for 2.5mS x 60 = 150mS

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

;Set All as 3st via TRISIO, Letting LED acumilate charge-

;			 bit: 76543210

MOVLW	b'11111111'

MOVWF	TRISIO

BCF     STATUS,RP0      ; Back to Bank 0   <<--+--###

;------------------------------------------

;Charge LED Cap-

MOVLW	d'20'		; 2 sec delay to charge LED...

Call	DLY_X		;delay for 100mS/loop

;------------------------------------------

;Now Start Reading LED-

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

;			 bit: 76543210 (Low 4 bits selcet enabled channel/s)

MOVLW   b'01010010'     ;AN1 enabled as Analog for ADC

; Set ADC Clock - Osc/16 = 4uS (1.6uS is minimum, but 4uS assures opperation at less than 3 Vdc.)

; Select/Enable Analog Channels (AN-1)

MOVWF   ANSEL

BCF     STATUS,RP0      ; Back to Bank 0   <<--+--###

;	-------------------------------------------------------

;			 bit: 76543210 (bit 2,3 select channel to convert from)

MOVLW   b'10000101'

; Set: RIGHTT-JUSTIFIED, Vref to Vdd, Select Chanel AN-1, turn on ADC

MOVWF   ADCON0

; The minimum acquisition time is 20uS for the Sample & Hold capacitor to settle,

MOVLW	d'2'		;5ms

Call	DLY_L		;delay for 2.5mS/loop

;Start ADC Conversion by turning GO/Done, bit-1 ON.

BSF		ADCON0,1

MOVLW	d'60'

Call	DLY_L		;delay for 2.5mS x 60 = 150mS

;-------------------------------------

;Conversion takes Min. 11 x ADC Clock = 11x4uS = 44uS:

ADCDLY2:

;		MOVLW	d'6'

MOVLW	d'20'	;try 200us

Call	DLY_S		;delay for 10uS/loop

;Check for conversion complete:

BTFSC	ADCON0,1		;Skip next if 'DONE'bit = 0 ; Conversion Complete.

GOTO	ADCDLY2			;Delay again till conversion is complete, or WDT resets...

; Conversion Complete- Battery Status Value is now in 'ADRESH'; Turn off ADC.

;	-------------------------------------------------------

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

MOVF	ADRESL,W	;Get voltage level into 'W'

BCF     STATUS,RP0      ; Back to Bank 0   <<--+--###

Return

;=============================================================================

;=============================================================================

;-------------------------------------------------------

PwrDwn:

MOVLW   b'00000111'     ; Turn Comparitor OFF, Lowest Power consumption.

MOVWF   CMCON           ;  by setting CMCON<0:3>

CLRF	GPIO

BSF     STATUS,RP0      ; Set Bank 1   <<--+--###

CLRF	ANSEL			;Deselect all analog input channels to save power.

MOVLW	b'11111111'		; Set All bits to High Imp.input state-

MOVWF	TRISIO

BCF     STATUS,RP0      ; Back to Bank 0   <<--+--###

Return

;NOTE:

;  All ports should be in High Impedence state.

;(TRIS bit=1, Port bit is High Impedence)

;NOTE:

;  Both the comparator and voltage reference, if enabled

; before entering SLEEP mode, remain active during

; SLEEP. This results in higher SLEEP currents than

; shown in the power-down specifications. The

; additional current consumed by the comparator and the

; voltage reference is shown separately in the specifications.

; To minimize power consumption while in SLEEP

; mode, turn off the comparator, CM2:CM0 = 111, and

; voltage reference, VRCON<7> = 0.

;=============================================================================

;=============================================================================

;-------------------------------------------------------

;Extra-Long Delay - 'W' passes number of loops, 100ms ea

;Delays: 100ms to 25.5sec

DLY_X:	MOVWF	XLNG_CNT		;Store number of 100ms loops- Max delay: 25.5sec

MOVLW	D'40'		;Set 40 loops at..

CALL	DLY_L		;  2.5ms per loop

DECFSZ	XLNG_CNT,f		;If not 0, Execute next; If =0, Skip Next

GOTO	$-3				;Run DELAY again

RETURN

;------------------------------------------

;Long Delay - 'W' passes number of loops, 2.5ms ea

;Delays: 2.5ms to .637ms

DLY_L:	MOVWF	MID_CNT		;Store number of 2.5ms loops- Max delay: 637.5ms

MOVLW	D'250'	;Set 250 loops at..

CALL	DLY_S	;  10us per loop

DECFSZ	MID_CNT,f	;If not 0, Execute next; If =0, Skip Next

GOTO	$-3			;Run DELAY again

RETURN

;------------------------------------------

;Delay - 'W' passes number of loops, 10us ea

;Delays: 10 us to 2.55 ms

; Number of Delay loop passed in W & stored in DLY_CNT. Delay is

;  ( 3 + (DLY_CNT * 10)) * 1us/Cycle = Delay

;With the 4mhz internal clock, 1 cycle is 1us

;  Max delay is 3 + 255*10 = 2553 Cycles = 2.553ms	   Cycles

DLY_S:	MOVWF   DLY_CNT ; Store loop cnt passed in 'W'	(1)

D1_LOOP:

CALL	RetDLY		;4 Cycles					(4)

;        GOTO	$+1			;2 Cycles						(2)

;        GOTO	$+1			;2 Cycles						(2)

;        NOP					;							(1)

CLRWDT					;Clear WDT				(1)

D2_LOOP:

DECF    DLY_CNT,F       ; Subtract 1            (1)

INCFSZ  DLY_CNT,W       ; Check for underflow   (2)

GOTO    D1_LOOP          ; Not zero so loop     (2)

RetDLY:		;Call this Return 'SUB' to delay 4 clock cycles:

RETURN        			;						(2)

;=============================================================================

;=============================================================================

;-------------------------------------------------------

; Get sensor value & output the decimal number between 0 & 255 as 'beeps':

;Low beep= Zero, One high beep for digit count

; Pause between digits

;End with decending tones

;*********************************************************

MOVWF		OutByt		;Save for converstion...

;------------------------------------------------------------------

;Convert value passed in OutByt to 3 Decimal Digits:

DeciDig:

CLRF		Ac100s			;clear the 100's counter

CLRF		Ac10s			;clear the 10's counter

Sub100:

MOVLW		d'100'			;Check 100's		 (X)

SUBWF		OutByt,W		;				(Y)-(X)=>'W'

BTFSS		STATUS,Carry	;If Carry is set, Number is > 100

GOTO		Sub10			;try 10's

MOVWF		OutByt			;Save reduced value,

INCF		Ac100s,F

GOTO		Sub100

Sub10:			;OutByt still has 10s,1s.....

MOVLW		d'10'			;Check 10's		 (X)

SUBWF		OutByt,W		;				(Y)-(X)=>'W'

BTFSS		STATUS,Carry	;If Carry is set, Number is > 10

GOTO		DigDone

MOVWF		OutByt			;Save 1'0s

INCF		Ac10s,F

GOTO		Sub10

DigDone:	;OutByt is now 1's

;------------------------------------------------------------------

; Now, sound Beeps for Digits-

CALL	DigBeep			;Convert 100's in Ac100s,

MOVLW	d'10'		;~1 Sec Delay Between Digits

CALL	DLY_X		;100ms/Cycle

MOVF	Ac10s,W

MOVWF	Ac100s

Call	DigBeep			;Convert 10s in Ac10s,

MOVLW	d'10'		;~1 Sec Delay Between Digits

CALL	DLY_X		;100ms/Cycle

MOVF	OutByt,W

MOVWF	Ac100s

Call	DigBeep			;,and 1s in OutByt.

MOVLW	d'5'		;~1/2 Sec Delay Between Digits

CALL	DLY_X		;100ms/Cycle

;		 Call	 HalfSecx		;~.5 Sec Delay Between Digits

;		  GOTO	  RptTests			;Repeat tests...

RETURN

;------------------------------------------------------------------

; Convert number passed in Ac100s to Beeps; If Zero, sound 1 low tone

DigBeep:

MOVF		Ac100s,F		;Move to self- Set Zero bit in status...

BTFSS		STATUS,Z  	;If Zero is set, skip and send Zero Beep

GOTO		ToneBit			;If Carry is Clear, not zero, sound Beeps...

CALL		Tone0			;Sound Low note -Zero

RETLW	0

ToneBit:

MOVLW	d'1'

SUBWF	Ac100s,F

BTFSS		STATUS,Carry	;If Carry is set, all 100's sent

RETLW	0			;No digits, return...

Call	Tone1

MOVLW	d'5'		;~1/2 Sec Delay Between Digits

CALL	DLY_X		;100ms/Cycle

;		CALL	HalfSecx

GOTO	ToneBit

;- - - - - - - - - - - - - - - - - - - - - - - - - - - - -

;--------------------------------------------------

;

;		ORG		0x3c0

;		da		"(c)2007 Applied Inspirations, LLC"

ORG		0x3DA

DT		" "

DT		"("

DT		"c"

DT		")"

DT		"2"

DT		"0"

DT		"0"

DT		"7"

DT		" "

DT		"A"

DT		"p"

DT		"p"

DT		"l"

DT		"i"

DT		"e"

DT		"d"

DT		" "

DT		"I"

DT		"n"

DT		"s"

DT		"p"

DT		"i"

DT		"r"

DT		"a"

DT		"t"

DT		"i"

DT		"o"

DT		"n"

DT		"s"

DT		","

DT		" "

DT		"L"

DT		"L"

DT		"C"

DT		" "

;********************************************************************************************

END

;XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

.	.	.